## Slide 1
Pipelining UNIT II – Chapter 3
Reference :
Appendix A,
Computer Architecture, A Quantitative Approach – John L. Hennessey and David A. Patterson

## Slide 2
Introduction

## Slide 3
Pipelining: Its Natural!
Laundry Example
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, and fold
  Washer takes 30 minutes
  Dryer takes 40 minutes
  “Folder” takes 20 minutes
A
B
C
D

## Slide 4
Sequential Laundry
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time

## Slide 5
Pipelined Laundry Start Work
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 6
Computer Pipelines
Pipelining is an implementation technique whereby multiple instructions are overlapped in execution; it takes advantage of parallelism.
In a computer pipeline, each step in the pipeline completes a part of an instructions.
Different steps are completing different parts of different instructions in parallel.
Each of these steps is called a pipe stage or a pipe segment
The stages are connected one to the next to form a pipe
The throughput of an instruction pipeline is determined by how often an instruction exits the pipeline

## Slide 7
Computer Pipelines
Pipeline properties
  Execute billions : throughput is what matters.
  Processor cycle The time required between moving an instruction one step down the pipeline
  Processor cycle is determined by slowest pipeline stage;
The time per instruction on the pipelined processor in ideal conditions is equal to,

## Slide 8
The Basics of a RISC Instruction Set
Default RISC architecture is MIPS.
Few key properties of RISC architecture
-The only operations that affect memory are load and store operations that move data from memory to a register or to memory from a register, respectively.
Most RISC architectures, like MIPS, have three classes of instructions:
ALU instruction
Load and store instructions,
Branches and jumps

## Slide 9
A Simple Implementation of a RISC Instruction Set
Every instruction can be implemented in at most 5 clock cycles
  Instruction fetch cycle (IF): send PC to memory, fetch the current instruction from memory, and update PC to the next sequential PC by adding 4 to the PC.
  IR<-Mem[PC]
  NPC<-PC+4
  Instruction decode/register fetch cycle (ID): decode the instruction, read the registers corresponding to register source specifiers from the register file.
  Execution/effective address cycle (EX): The ALU operates on the operands prepared in the prior cycle.
-Perform one of three functions
  Memory reference, Register-Register ALU instruction and Register-Immediate ALU instruction.

## Slide 10
A Simple Implementation of a RISC Instruction Set
Memory reference:
ALU output <- A +Imm
-The ALU adds the base register and the offset to form the effective address.
• Register-Register ALU instruction:
ALU output <- A OP B
-The ALU performs the operation specified by the ALU opcode on reg A and B
• Register-Immediate ALU instruction:
ALU output <- A OP Imm
-The ALU performs the operation specified by the ALU opcode on the register A e and immediate.
  ALU output <- NPC + Imm

## Slide 11
  Memory access (MEM): perform load/store instructions.
If the instruction is a load, memory does a read using the effective address computed in the previous cycle.
If it is a store, then the memory writes the data from register file using the effective address.
  Write-back cycle (WB): Register-Register ALU instruction or Load instruction.
Write the result into the register file, whether it comes from the memory system (for a load) or from the ALU

## Slide 12
Classic 5-Stage Pipeline for a RISC
Each cycle the hardware will initiate a new instruction and will be executing some part of the five different instructions
  However, be ensure that the overlap of instructions in the pipeline cannot cause such a conflict. (also called Hazard)
Clock number |  |  |  |  |  |  |  |  | 
Instruction number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Instruction i | IF | ID | EX | MEM | WB |  |  |  | 
Instruction i+1 |  | IF | ID | EX | MEM | WB |  |  | 
Instruction i+2 |  |  | IF | ID | EX | MEM | WB |  | 
Instruction i+3 |  |  |  | IF | ID | EX | MEM | WB | 
Instruction i+4 |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 13
Series of Data Path

## Slide 14
Three observations on which this fact rests.
Separate instruction and data memories, with separate instruction and data caches
-Eliminates a conflict between instruction fetch and data memory access.
The register file is used in the two stages: one for reading in ID and one for writing in WB.
Does not deal with the PC, IF stage in preparation for the next instruction

## Slide 15
Ensure that instructions in different stages of the pipeline do not interfere with one another
introducing pipeline registers between successive stages of the pipeline
End of a clock cycle all the results from a given stage
are stored into a register that is used as the input to the next stage on the next clock cycle.

## Slide 17
Pipelining Performance (1/2)
Pipelining increases throughput, not reduce the execution time of an individual instruction.
  In fact, slightly increases the execution time (an instruction) due to overhead in the control of the pipeline.
  Practical depth of a pipeline is limits by increasing execution time.
Pipeline overhead
  Unbalanced pipeline stage;
  Pipeline stage overhead;
  Pipeline register delay;
  Clock skew.

## Slide 18
Performance of Pipelines with Stalls
A stall causes the pipeline performance to degrade from the ideal performance.

## Slide 21
Exercise
Example : Consider an unpipelined processor. Assume that it has a 1 ns clock cycle and that it uses
4 cycles for ALU operations and branches
5 cycles for memory operations.
Assume that the relative frequencies of these operations are 40%, 20%, and 40% respectively.
Suppose that due to clock skew and set up, pipelining the processor adds 0.2 ns of overhead to the clock.
Ignoring any latency impact, how much speed up in the instruction execution rate will we gain from pipeline?

## Slide 22
Answer
The average instruction execution time on the unpipelined processor is
Average instruction execution time = Clock cycle x Average CPI
= 1 ns x ((40% + 20%) x 4 + 40% x 5)
= 1 ns x 4.4 = 4.4 ns

## Slide 23
Contd..
The average instruction execution time on the pipelined processor is
= speed of the Slowest stage + overhead
= 1 + 0.2 = 1.2 ns.
Speedup from pipelining = Avg. instruction time unpipelined / Avg. instruction time pipelined
= 4.4 ns / 1.2 ns = 3.7 times

## Slide 24
24
A.2 The Major Hurdle of Pipelining – Pipeline Hazard
Limits to pipelining: there are situations, called Hazards, prevent next instruction from executing during its designated clock cycle, thus reduce the performance from the ideal speedup.
Three classes of hazards are:
  Structural hazards: arise from resource conflicts when the hardware cannot support all possible combinations of instructions simultaneously in overlapped execution- two different instructions use same h/w in the same cycle .
  Data hazards: arise when an instruction depends on result of prior instruction still in the pipeline, RAW, WAR and WAW.
  Control hazards: Pipelining of branches & other instructions that change the PC.
  Common solution is to stall the pipeline until the hazard is cleared, i.e., inserting one or more “bubbles” in the pipeline.

## Slide 25
Structural Hazards
In pipelined processor, if some combination of instructions cannot be accommodated because of resource conflicts, the processor is said to have a structural hazard.
Arises when a
  functional unit is not fully pipelined
  resource is not duplicated enough
  Ex:1) pipeline want to perform two writes in a clock cycle one with processor of one register-file write port,
2)processor with shared a single-memory pipeline for data
and instructions.
Solution :
To resolve the hazard, the pipeline is stalled until the required unit is available
Pipeline stalls increase the CPI

## Slide 26
One Memory Port - Structural Hazards -a Load with one memory port -conflict arises whenever a memory reference occurs
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
MEM
MEM
Reg
Reg
ALU
MEM
EM
M
Reg
Reg
ALU
MEM
MEM
Reg
Reg
ALU
MEM
MEM
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
MEM
MEM
Reg
Notes: CS252 S05
26

## Slide 27
One Memory Port/Structural Hazards (Similar to Figure A.5, Page A-15)
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
MEM
MEM
Reg
Reg
ALU
MEM
MEM
Reg
Reg
ALU
MEM
MEM
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
MEM
MEM
Reg
Bubble
Bubble
Bubble
Bubble
Bubble
Notes: CS252 S05
27

## Slide 29
29
Data Hazards
Data hazards occur when the pipeline changes the order of read/write accesses to operands (registers) so that the order differs from the order seen by sequentially executing instructions on an unpipelined processor.
Where there’s real trouble is when we have:
  instruction A
  instruction B,
and B manipulates (reads or writes) data before A does. This violates the order of the instructions, since the architecture implies that A completes entirely before B is executed.

## Slide 31
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Data Hazard on R1
Time (clock cycles) 1 2 3 4 5 6 7 8
IF
ID/RF
EX
MEM
WB
Notes: CS252 S05
31

## Slide 32
Three Generic Data Hazards
Read After Write (RAW) InstrJ tries to read operand before InstrI writes it
Write After Read (WAR) InstrJ writes operand before InstrI reads it
Write After Write (WAW) InstrJ writes operand before InstrI writes it.

## Slide 33
Minimizing Data Hazard Stalls by Forwarding
If the result can be moved from the pipeline register where the ADD stores it to where the SUB needs it, then the need for a stall can be avoided.
1. The ALU result from both the EX/MEM and MEM/WB pipeline registers is always fed back to the ALU inputs.
2. If the forwarding hardware detects previous ALU operation has written the register corresponding to a source for the current ALU operation control logic selects the forwarded result as the ALU input rather than the value read from the register file.

## Slide 34
Time (clock cycles) 1 2 3 4 5 6 7 8
Forwarding to Avoid Data Hazard Figure A.7, Page A-19
I
n
s
t
r
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DM
iIM
Reg
Reg
ALU
DM
IM
Reg
Reg
ALU
DM
iIM
Reg
Reg
ALU
DM
iIM
Reg
Reg
ALU
DM
iIM
Reg
Notes: CS252 S05
34

## Slide 36
36
There are some instances where hazards occur, even with forwarding, e.g., the data isn’t loaded until after the MEM stage.
I
n
s
t
r.
O
r
d
e
r
LD R1,0(R2)
DSUB R4,R1,R6
AND R6,R1,R7
OR R8,R1,R9
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Data Hazards Requiring Stalls
Time (clock cycles)
CC1
CC2
CC3
CC4
CC6
CC7
CC5
CC8
Notes: 36

## Slide 37
Time (clock cycles) 1 2 3 4 5 6 7 8
I
n
s
t
r
O
r
d
e
r
Ld r1, 0(r2)
dsub r4,r1,r5
and r6,r1,r7
or r8,r1,r9
Data Hazard Even with Forwarding Figure A.9, Page A-21
Reg
ALU
DM
IM
Reg
Reg
ALU
DM
IM
Reg
Reg
ALU
DM
IM
Reg
Reg
ALU
DM
IM
Reg
HAZARD
Notes: CS252 S05
37
MIPS actutally didn’t interlecok: MPU without Interlocked Pipelined Stages

## Slide 38
38
OR R8,R1,R9
I
n
s
t
r.
O
r
d
e
r
LD R1,0(R2)
DSUB R4,R1,R5
AND R6,R1,R7
Reg
ALU
DMem
Ifetch
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Ifetch
ALU
DMem
Reg
Bubble
Reg
Ifetch
ALU
DMem
Bubble
Reg
Data Hazards Requiring Stalls
The stall is necessary for the case.
Time (clock cycles)
CC1
CC2
CC3
CC4
CC6
CC7
CC5
CC8
Notes: 38

## Slide 39
39
LD R1, 0(R2) | IF | ID | EX | MEM | WB |  |  | 
DSUB R4, R1, R5 |  | IF | ID | EX | MEM | WB |  | 
AND R6, R1, R7 |  |  | IF | ID | EX | MEM | WB | 
OR R8, R1, R9 |  |  |  | IF | ID | EX | MEM | WB
LD R1, 0(R2) | IF | ID | EX | MEM | WB |  |  |  | 
DSUB R4, R1, R5 |  | IF | ID | stall | EX | MEM | WB |  | 
AND R6, R1, R7 |  |  | IF | stall | ID | EX | MEM | WB | 
OR R8, R1, R9 |  |  |  | stall | IF | ID | EX | MEM | WB
Another Representation of the Stall
In the top table, we can see why a stall is needed: The MEM cycle
of the load produces a value that is needed in the EX cycle of the
DSUB, which occurs at the same time. This problem is solved by
inserting a stall, as shown in the bottom table.
Notes: 39

## Slide 40
Control hazard or Branch Hazard
Cause a greater performance loss for our MIPS pipeline than do data hazards
When a branch is executed, it may or may not change the PC to something other than its current value plus 4
if a branch changes the PC to its target address, it is a taken branch ,if it falls through, it is not taken.
If instruction i is a taken branch, then the PC is normally not changed until the end of ID.
redo the fetch of the instruction following a branch, once we detect the branch during ID.
One stall cycle for every branch will yield performance loss of 10% to 30% depending on the branch frequency

## Slide 41
Number of clock cycle in branch stall can be reduced by
1.Find out whether branch is taken or not earlier in the pipeline
2.Compute the taken PC (address of branch target)

## Slide 42
42
Four Solutions to Branch Hazards
#1: Stall until branch direction is clear
  Simple both for software and hardware
  Branch penalty is fixed (1-cycle penalty for revised MIPS)
Branch instr. | IF | ID | EX | MEM | WB |  |  |  | 
Branch successor |  | IF | IF | ID | EX | MEM | WB |  | 
Branch successor+1 |  |  |  | IF | ID | EX | MEM | WB | 
Branch successor+2 |  |  |  |  | IF | ID | EX | MEM | WB
Notes: 42

## Slide 43
43
Four Solutions to Branch Hazards
Untaken branch instr. | IF | ID | EX | MEM | WB |  |  |  | 
Branch successor |  | IF | ID | EX | MEM | WB |  |  | 
Branch successor+1 |  |  | IF | ID | EX | MEM | WB |  | 
Branch successor+2 |  |  |  | IF | ID | EX | MEM | WB | 
Branch successor+3 |  |  |  |  | IF | ID | EX | MEM | WB
Taken branch instr. | IF | ID | EX | MEM | WB |  |  |  | 
Branch successor |  | IF | idle | idle | idle | idle |  |  | 
Branch target |  |  | IF | ID | EX | MEM | WB |  | 
Branch successor+1 |  |  |  | IF | ID | EX | MEM | WB | 
Branch successor+2 |  |  |  |  | IF | ID | EX | MEM | WB
#2: Predict Branch Not Taken
  Continue to fetch instructions as if the branch were a normal instruction.
  If the branch is taken, turn the fetched instruction into a no-op and restart the fetch at the target address.

## Slide 44
44
Four Solutions to Branch Hazards
#3: Predict Branch Taken
  As soon as the branch is decoded and the target address is computed, we assume the branch to be taken and begin fetching and executing at the target.
  But haven’t calculated the target address before we know the branch outcome in MIPS
    MIPS still incurs 1-cycle branch penalty
    Useful for other machines on which the target address is known before the branch outcome

## Slide 45
45
#4: Delayed Branch
  The execution cycle with a branch delay of one is
  branch instruction sequential successor1 branch target if taken
  The sequential successor is in the branch delay slot.
  The instruction in the branch delay slot is executed whether or not the branch is taken (for zero cycle penalty)
Four Solutions to Branch Hazards
Notes: 45

## Slide 46
Performance of Branch Schemes

## Slide 47
How Is Pipelining Implemented?
A Simple Implementation of MIPS

## Slide 52
Linear pipeline processors and Non-linear pipeline processors
Reference :
Chapter-6
Advanced Computer Architecture Parallelism, Scalability – Kai Hwang

## Slide 53
Linear Pipeline Processor
Linear pipeline processes a sequence of subtasks with linear precedence
Linear pipeline processor is cascade of processing stages which are linearly connected
Data flowing in streams from stage S1 to the final stage Sk
Two types of linear pipelines based on Control of data flow : synchronous or asynchronous Modes

## Slide 54
Linear Pipeline Processor
S1
S2
Sk
   

## Slide 55
Linear Asynchronous Pipeline

## Slide 56
Linear Synchronous Pipeline

## Slide 57
Reservation Table for a 3-stage Linear Pipeline
S3
S2
S1
X
X
1
2
3
Time (clock cycles)
Full pipeline after 3 cycles
X
Stages

## Slide 58
Nonlinear Pipelining
Nonlinear pipeline: Which allows feedback and feed forward connections in addition to streamline connections.

## Slide 59
Nonlinear Pipelining
Nonlinear pipeline: Which allows feedback and feed forward connections in addition to streamline connections.
A three stage nonlinear pipeline.

## Slide 60
Reservation tables are two-dimensional charts used to show how successive pipeline stages are utilized (or reserved) for a specific function
Evaluation Time: Number of Columns in reservation table
Reservation table for function X
Reservation table for function Y
S2
S1
S3
8
7
6
5
4
3
2
1
S2
S1
S3
6
5
4
3
2
1
Let X & Y be two functions evaluating in the above pipeline.

## Slide 61
Nonlinear Pipelining
Latency: number of time units (clock cycles) between two initiations of a pipeline is the latency between them.
Collision: resource conflicts between two initiation in the pipeline.
Forbidden latency: Latency that cause collision.
Permissible Latency: Latency that will not cause collision
MAL: minimal average latency (MAL) that will give maximum efficiency of pipeline without collisions.
Latency Analysis

## Slide 62
Collision vector: (collision array) is a combined set of permissible and forbidden latencies.
C = ( Cm Cm-1 …… C2 C1 )
Where Cm must always be 1
Size must be equal to size of the forbidden latency
M : maximum forbidden latency
Ci : 0  permissible
Ci : 1  forbidden

## Slide 63
.
Find out permissible and forbidden latencies of the reservation table for function x. Also design the collusion vector and state transition diagram for collision vector.
S2
S1
S3
8
7
6
5
4
3
2
1
Q

## Slide 64
F.Lx = 2,4,5,7
Cx = 1011010
M : maximum forbidden latency
Ci : 0  permissible
Ci : 1  forbidden
P.Lx = 1,3,6,8
C = ( Cm Cm-1 …… C2 C1 )
Where Cm must always be 1

## Slide 65
Nonlinear Pipelining
Latency Analysis
1011010
Starting state
First bit (zero bit) to be right shifted
1111111
Current state.

## Slide 66
Nonlinear Pipelining
Latency Analysis
1011010
1111111
1011011

## Slide 67
Nonlinear Pipelining
Latency Analysis
1011010
1111111
1011011
Now, right shift the sixth bit and see what you get after ORing it with the start state..

## Slide 68
Nonlinear Pipelining
Latency Analysis
1011010
1111111
1011011
Since there are no more zeros left in this state to be right, lets move on to the next state.
Now this state is our current state.

## Slide 69
So we get,
Nonlinear Pipelining
Latency Analysis
In this state we don’t have any zeros, so we move on to the next state, as our current state.
Right shifting and ORing of the third and sixth bit gives the same state again.

## Slide 70
Nonlinear Pipelining
Latency Analysis
1011010
1111111
1011011
One last thing, when the number of shifts is m+1 (m: maximum forbidden latency), all the transitions are redirected back to initial state.
And mark the minimal latencies with *

## Slide 71
Nonlinear Pipelining
Latency Analysis
The next step is to write the simple latency cycles.
Some of these are called greedy cycles

## Slide 72
Greedy Cycles: are those ones whose edges are all made with minimum latencies from their respective states (ones with *) .
Nonlinear Pipelining
Latency Analysis

## Slide 73
Nonlinear Pipelining
Latency Analysis
Q. Design the collusion vector and state transition diagram for the below case.

## Slide 74
Cy =1010
F.Ly = 4,2 & P.Ly = 1,3,5,6.

## Slide 75
Collision Free Scheduling for Y
1 0 1 0
m….2 1
Collision vector for Y
1 : collision
0 : no collision
1 0 1 0
1 0 1 1
1 1 1 1
3*
5+
5+
5+
1*
3

## Slide 76
Compute simple cycle and greedy cycle for the below scenario
1 0 1 0
1 0 1 1
1 1 1 1
3
5+
5+
5+
1
3

## Slide 77
Simple cycle (3),(5),(1,5),(3,5)
Greedy cycle (1,5) and (3)
MAL is 3

## Slide 78
Evaluate the function X, draw the reservation table for the latency 2 and latency 5, identify the stages of forbidden.
S2
S1
S3
8
7
6
5
4
3
2
1

## Slide 79
Consider the same pipeline, lets see initiations in the pipeline for function X, with latency=2

## Slide 80
Consider the same pipeline, lets see initiations in the pipeline for function X, with latency=5

## Slide 81
Nonlinear Pipelining
Efficiency of Nonlinear Pipelining:
We find the efficiency of nonlinear pipeline using greedy cycle corresponding to MAL.
100% efficiency: when all the stages of pipeline are always busy.

## Slide 82
S2
S1
S3
8
7
6
5
4
3
2
1
Q. Calculate efficiency for the pipeline function of x with greedy cycle 3.

## Slide 84
S2
S1
S3
8
7
6
5
4
3
2
1
9
10
11
12
13
15
14
The time until there appears no match is called the Setup Time.
setup time
Calculating the efficiency: With in a frame we have,
Total stages=9
Stages busy=8 (take from the matched frames)

## Slide 85
efficiency:  = x 100
Q. Calculate efficiency for the same pipeline with greedy cycle (1,8).
 = x 100
= 88.89%

## Slide 87
S2
S1
S3
8
7
6
5
4
3
2
1
9
10
11
12
13
14
15
16
17
18
Calculating the efficiency: With in a frame we have,
Total stages=27
Stages busy=16
matched

## Slide 88
= 59.23%

## Slide 89
Draw the block diagram of 5 stage MIPS pipeline. Explain the operations performed by every pipe stage for the execution of instruction SUB R1, R2, R3.
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
MUX
Data
Memory
MUX
Sign
Extend
Zero?
IF/ID
ID/EX
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
Next SEQ PC
RD
RD
RD
WB Data
Data stationary control
  local decode for each instruction phase / pipeline stage
Next PC
Address
RS1
RS2
Imm
MUX

## Slide 91
Notes: CS252 S05
91

## Slide 92
CPU time= IC x CPI x Cycle time
Cycle time T=1/f

## Slide 93
Calculate CPI:
CPI= (0.35*1) + (0.25*2) + (0.15*2) + (0.25*3) =1.9
Since the frequency is given-> Cycle time T=1/f = 1/109
Calculate CPU Time:
CPU time= IC x CPI x Cycle time
= 1000000 x 1.9 x 10-9 =1.9 x 10-3 = 1.9 msec

## Slide 94
Clocking and Timing Control:Linear Synchronous pipeline
Si
Si+1

m
d
Clock cycle of the pipeline : 
i : Time delay of circuitry stage Si
d:Time delay of latch
 = max {m } + d
m :Maximum stage delay
Pipeline frequency : f
f = 1 / 

## Slide 95
Speedup and Efficiency
k-stage pipeline processes n tasks in k + (n-1) clock cycles:
k cycles for the first task and n-1 cycles for the remaining n-1 tasks
Total time to process n tasks
Tk = [ k + (n-1)] 
For the non-pipelined processor
T1 = n k 
Speedup factor

## Slide 96
Efficiency and Throughput
Efficiency of the k-stages pipeline :
Ek =
Sk
k
=
n
k + (n-1)
Pipeline throughput (the number of tasks per unit time) :
note equivalence to IPC
Hk =
n
[ k + (n-1)] 
=
n f
k + (n-1)

## Slide 97
Pipeline Performance: Example
Task has 4 subtasks with time: t1=60, t2=50, t3=90, and t4=80 ns (nanoseconds)
latch delay = 10 calculate

## Slide 99
END of Unit II